## Slide 1: Two-player Tic-Tac-Toe
Kyle Jonas
Karina Cuadrado
Team 2C
CMPEN 371: Final Project

## Slide 2: Introduction
Objective
Design and implement a two-player Tic-Tac-Toe game displayed through VGA with keyboard interaction (keypad assign to game board positions)
Design overview
Split top-module into 2 internal sub components: VGAControl and GameControl.
1 2 3
4 5 6
7 8 9
Game board positions:

## Slide 3: Top-level design

## Slide 4: Game control module

## Slide 5: Turn Control State Diagram
Ready: Waits for new keypress
New Code: Checks for break/multi key
Translate: On #1-9 keeps track of board location
Output: Checks if game board is empty and then assigns player to location, alternates turn

## Slide 6: Player Logic
Major signals
  Three 9 bit signals for P1, P2 and game board
  2 bit win signal
On keypress, checks for #1-9
Compare # to Game Board bit
  If empty, sets bit to 1, sets player signal bit to 1, then alternates turn
  If full, falls back to state waiting for new keypress
Checks all possible win combinations
Passes P1, P2, and win to VGA controller

## Slide 7: VGA control module

## Slide 8: Drawing Game Pieces
VGA control module checks player 1 and player 2 signals to see where game pieces need to be drawn.

## Slide 9: Working features of design
Reset of game board
No overwriting of other player’s piece
Mapped keypad (1-9) with positions on 3x3 game board
Displayed users whose turn is it with LED
Display user what key they have pressed on LEDs
Displayed game on VGA with colors to distinguish players
Win detection

## Slide 10: Reliability
Full game functionality
Players can’t can't overwrite other game pieces or place new pieces after a game has been won
Only performance problem is some monitors show thin lines in the background.
  Issue with pixel clock in some monitors

## Slide 11: Video - Demo

## Slide 12: Possible features to be added in future
One player Tic-Tac-Toe
  Have user play against AI
Score tracking
  Display count of wins per user on 7 segment displays

## Slide 13: Conclusion
Challenges faced
  VGA
  Putting it all together
What we learned
  Implementation of multiple interfaces
Successful completion of project

## Slide 14: References
PS2 Keyboard from class
VGA control and VGA drive modules modified from Rob Chapman, University of Alberta.
Chapman, Rob . “VHDL VGA Driver.” University of Alberta, Department of Electrical and Computer Engineering, www.ece.ualberta.ca/~elliott/ee552/studentAppNotes/1998_w/Altera_UP1_Board_Map/vga.html.